## Slide 1: Renewable energy for residential buildings Dietmar Bässler, energy craftsman

## Slide 2: Renewable energy sources (RES) for residential buildings
Energy demand in residential buildings
RES-technology and systems for energy supply of buildings
Efficacy and efficiency
system integration
System combination
summery
content

## Slide 3: What and where?
Energy demand in residential buildings
ca. 85%
ca. 85%
Der Energiebedarf der Heizung wird unterschätzt

## Slide 4
Electricity from photovoltaic (PV)
Electricity and heat from CHP
Electricity from small wind turbines
Diversity of systems
RE technology for building energy supply
Heat from solar thermal
Heat from biomass (Wood, pellets, wood chip heating systems)
Heat from heat pumps

## Slide 5
conditions
RES systems for building energy supply
Criteria on site:
Structural situation
  Roof, roof orientation, utility room, boiler room, heat distribution
Living conditions of the inhabitants and users
  Automatic-manual mode (firewood, ash, etc.)
Wishes and financial possibilities of the customer
  possibly divided into several stages of the project

## Slide 6
You have the choice
RES systems for building energy supply
Criteria for system selection:
Energy sources with no or the lowest energy cost
  Sun (solar energy + solar thermal), pellets, wood, wood chips, etc.
Devices with high efficiency and more efficient use of energy
  High efficiency in partial load operation
Integration into the overall system
  Are future enhancements and supplements possible?
Combination of equipment and systems
  Smart combinations with the aim RES = 100%, energy costs = 0,- €

## Slide 7: Efficiency and utilization counts
  High efficiency at part load

time in use is increased by up to 4 hrs. per day
energy output increases by 5 - 10%
Ex. solar power - Inverter
WR 1
turn-on
> 188 V DC
turn-on
> 250 V DC

bis 15 hrs.
bis 11 hrs.
WR 2

## Slide 8: Efficiency and utilization counts
  High efficiency at part load

Large operating range with high efficiency
Very low emissions
Ex. Wood
Gasification Boiler
with swirl combustion chamber
Standard combustor
operating range good at only one point
long heating period


## Slide 9: Efficiency and utilization counts
System integration is important

heat sources
Ex. Central buffer
heat consumers
Direct distribution of heat
Characteristics:
Direct distribution of heat
Central storage of heat
Fresh hot water
Heat sources operate independently of each other
Advantages:
Fast heat supply to consumers
Low Standby – losses
Very good combination possibilities
Anytime, easily extendable

## Slide 10: Efficiency and utilization counts
System integration is important

Increase of usage time
Energy saving up to about 50%
Energy saving up to 20%
Ex. Solar water heating

Var. 1
Var. 2
Memory heat storage /
Heat storage /

## Slide 11: Efficiency and utilization counts
System integration is important
Ex. PV system / solar power usage (overfeeding)
9,9 kWp
alignment:
East 10° + south 13° + west 10°
5,2 kWp
alignment: south-west 32°

Own efficiency about 50% Energy saving about 60% Electricity costs reduction with electricity sales 95%
+ battery storage
6,4 kWh

Own efficiency about 30% Energy saving about 20% Electricity costs reduction with electricity sales 45%
Var. 1
Var. 2

## Slide 12: Efficiency and utilization counts
Combination of systems
Ex. PV-conditioning / heat pump / solar thermal system
8,2 kWp PV
alignment: south 34°
10 m² solar thermal

Self-efficiency PV 12%
Percentage of e-energy and thus Energy saving about 80% (For PV power, ST-heat, WP-heat)
Energy costs per annum 680, - € (For House-power, WP-electricity, heat)
With electricity sales approximately -550, - €
9 kW
Heat pump
(air / water)

## Slide 13: Efficiency and utilization counts
Combination of systems
Ex. PV system / Electric storage heaters / electric storage for hot water
9,9 kWp
alignment:
East – West 30°
Home-Manager

Self-efficiency PV 40%
Percentage of e-energy and thus Energy saving about 50% (For PV power, PV-thermal, PV WW)
electrical storage heaters 8 kW
electrical underfloor heating 0,6 kW
electric storage for hot water2-6 kW

## Slide 14: summary
consider local situation   objective: use the variety of possibilities
using Renewable Fuels  objetive: Goal: no costs for energy
Devices with high efficiency  objective: high efficiency at partial load
integrate systems efficiently  objective: high efficiency!
combine systems smart  objective: low energy / operating costs!

## Slide 15
Ask dogmas in question!
Think cross!
And have fun!
Thank you for your attention

## Slide 16: energy cooperative & wind energy Jakob Schäfer, Murrhardt, Germany

## Slide 17: Aims of presentation
citizens energy cooperative in Murrhardt (EGM)
role of citizens energy cooperatives in Germany
planned wind farm project in Murrhardt (Zollstock-Springstein)

## Slide 18: citizens energy cooperative Murrhardt
Citizens solar power plants in Murrhardt since 2008
in the legal form of a limited partnership
shares available to hold from ~800 £ onwards
classical investment into renewable energy
security through guaranteed feed-in tariff

## Slide 19
in total 6 facilities
installed production capacity (kWp):
20, 22, 52, 20, 8, 32 (each in kWp)
in total 154 kWp

## Slide 20: about four weeks before Fukushima
energy cooperative Murrhardt (EGM) eG
founded on 15 February 2011
in the legal form of a cooperative
shares available to hold from ~76 £ onwards
availability for more members to participate through low costs

## Slide 21: agenda since 2011
Commitment in tender for new operator of the power grid in Murrhardt
  target not reached
Commitment in Murrhardt´s all new electricity grid operating company
  target not reached
Distribution of electricity through own local brand (support through partner company with experience in deregulated power market)
  target reached

## Slide 22: boom of energy cooperatives in Germany
within ten years growth
from ~ 50 to over 550

## Slide 23: recent projects and initiatives brief overview of dates in german energy policy
agreement 2002 to leave nuclear technology in Germany
extensional use agreed in 2010
few months later roll-back after Fukushima in March 2011
Energiewende and last shut down of german nuclear power plant in 2022
new provincial government in our province since 2011
complete change in provincial policy regarding use of wind energy

## Slide 24: location of planned wind farm
6 turbines
Nordex N 117 (2,4 MW)
3 Mio. £ per turbine
consortium of various
shareholders
estimated time of
building permit:
December 2014
Photo / picture

## Slide 25: visualization of the Springstein hill in Murrhardt
view from Siebenknie to Springstein
(everything within Murrhardt municipality)

## Slide 26: Conclusion
unexpected difficulties with state authorities hit´s our energy cooperative Murrhardt hard
still no clearance when building permit to expect
difficult to establish a profitable energy cooperative in Murrhardt
nevertheless engagement for climate justice with climate summit Paris 2015 in mind
strong will of civil society to move the energy sector in a innovative way forward