## Slide 1
River Power around Frome Anthony Battersby Chairman, Mendip Power Group

## Slide 2


*
*





Stowford
Tellisford
Shawford
Clifford
Staplemead
Croscombe
Witham Hole
Coleford
Bleadney
Burcott
Mendip Power Group
Lullington
Farleigh Hungerford

Ironstone

*
Hapsford
*
*
*

Iford
Farthingham

## Slide 3: Objectives of MPG
To install effective renewable energy generating systems.
To promote improved energy efficiency and increased development and use of renewable sources of power.
To attract funding to meet these objectives.

## Slide 4
Site | Capacity (kW) | Type
Dunkirk | 3 | crossflow
Farthingham | 55 | Archimedes screw
Hapsford | 58 | crossflow
Iford Manor | 44 | Archimedes screw
Lullington | 66 | Archimedes screw
Tellisford | 60 | Kaplan
Wallbridge | 12 | Francis
Burcott Mill | 10 | water wheel
Alhampton | 10 | Archimedes screw
Wookey Hole | 30 | Kaplan
Iwood Manor | 11 | crossflow
Littleton Mill | 28 | Francis
Total | 387 | 
Operational Hydropower Sites in Mendip

## Slide 5
Site | Capacity (kW) | Proposed Type
Clifford Hydro | 50 | propeller
Iron Mill | 75 | Kaplan
Stowford | 70 | Kaplan
Wadbury | 70 | Kaplan
West Lydford | 55 | Kaplan
Weavers Mill | 90 | Kaplan
Kingston Mill | 50 | Kaplan
Job's Mill | 10 | Kaplan
Total | 470 | 
Hydropower sites under development in Mendip

## Slide 6
Undeveloped sites | Capacity (kW)
23 | 670
Grand Total | 1,527
Hydropower sites existing but undeveloped

## Slide 7: Experience with Turbine Types
Chart: Output from River Frome Turbines (flow=4.3 cumecs) July 2012 to October 2015
| 66kW Screw, LF=43% | 55kW Kaplan, LF=56% | 44kW Screw, LF=17% | 54.99kW Screw, LF=26%
Output (kW) | 861 | 925.419 | 412 | 434
Head (m) | 2.3 | 1.7 | 1.64 | 1.75

## Slide 8: Constraints
1 Environment Agency Licensing
  Flood risk assessment
  Geomorphology study
  River corridor study
  Provision of fish pass (may cost £100,000)
  Screening for eels (proposed gauge 2mm, which will kill most hydro)
  Flow split at best 1.3 x mean flow, but may be less
2 Feed in Tariff
  Now one third of original (8.54p/kWh plus price of electricity exported 4.8p)
  Great uncertainty due to frequent changes
3 Cost
  Small scale hydro sites are expensive (£7,000-£10,000 per installed kW)

## Slide 9: Cost of installing Hydropower

## Slide 10: Further Information
  Anthony Battersby Tellisford Mill, Tellisford, Bath BA2 7RL, UK Telephone 44-(0)1373-830322
  E-Mail FBA@FBATM.BIZ